VPC
# CIDR – Ipv4
1. Classless Inter – Domain Routing – A method for allocating IP addresses
2. They help to define an IP address range:
  1. xx.xx.xx.xx/32 – here “32” represent 1 IP
  2. 0.0.0.0/0 – here “/0” represent all ip
  3. e.g. 192.168.0.0/26 – here 64 IP address are there – 192.168.0.0 to 192.168.0.63
3. Consist two components:
  1. Base IP
    1. Represent an IP contained in the range
    2. E.g. 192.168.0.0
  2. Subnet Mask
    1. How many bits can change in IP
    2. Example: /0, /24, /34
    3. Can take 2 forms:
      1. /8: 255.0.0.0
      2. /16: 255.255.0.0
      3. /24: 255.255.255.0
      4. /32: 255.255.255.255
## Subnet Mask
Allows part of the underlying IP to get additional next values from the base IP.
Ex:
1. 192.168.0.0/32 – allows for 1 IP (2^0)
2. 192.168.0.0/31 – allows for 2 IP (2 ^ 1)
3. 192.168.0.0/30 – allows for 4 IP (2 ^ 2)
## Public vs Private IP
1. Private IP can allow certain values
  1. 10.0.0.0 – 10.255.255.255 ( 10.0.0.0/8) – in big networks
  2. 172.16.0.0 – 172.31.255.255 (172.16.0.0/12) – AWS default VPC in that range
  3. 192.168.0.0 – 192.168.255.255 (192.168.0.0/16) – Home network

# Default VPC
1. New EC2 instances are launched into default VPC if not subset is specified
2. Default VPC has internet connectivity and all EC2 instances inside have public Ipv4 addresses
3. we also get a public and a private Ipv4 DNS names

# VPC in AWS
1. Soft limi – maximum 5 VPC / region
2. Max. CIDR/ VPC is 5, for each CIDR:
  1. Min. Size is /28 (16 IP addresses)
  2. Max. Size is /16 (65536 IP addresses)
3. Only Private Ipv4 ranges are allowed:
  1. 10.0.0.0 – 10.255.255.255 (10.0.0.0/8)
  2. 172.16.0.0 – 172.31.255.255 (172.16.0.0/12)
  3. 192.168.0.0 – 192.168.255.255 (192.168.0.0/16)
4. VPC CIDR should Not overlap with other networks.
## Creation of VPC
1. Name tag: Source-vpc
2. Ipv4 CIDR Block: 10.0.0.0/16 - 10.0.0.0 to 10.0.255.255
3. Tenancy: Default
4. Tags
## Subnets
1. AWS reserves 5 IP addresses (first 4 & last 1) in each subnet
2. These 5 IP addresses are not available for use and can’t be assigned to an EC2 instance.
3. Example: If CIDR block 10.0.0.0/24, then reserved IP addresses are:
  1. 10.0.0.0 – Networkd address
  2. 10.0.0.1 – reserved by AWS for the VPC router
  3. 10.0.0.2 – reserved by AWS for mapping to Amazon – provided DNS
  4. 10.0.0.3 – reserved by AWS for future use
  5. 10.0.0.255 – Network Broadcast Address. AWS does not support broadcast in a VPC therefore the address is reserved.
## Creation of Subnets
1. Vpc ID
2. Subnet Name
3. AZ
4. Ipv4 CIDR Block: 10.0.0.0/24

## Internet Gateway (IGW)
1. Allows resources in a VPC connect to the internet
2. It scales horizontally and is highly available and redundant
3. Must be created separately from a VPC
4. One VPC can only attached to one IGW and vice versa.
5. IGW on their own do not allow internet access.
6. Route table must also be edited

## Creation of Route Table and IGW
1. Lauch an EC2 instance.
  1. Go to network settings:
    1. Select your own VPC
    2. Select subnet
    3. Disable the auto – assign public IP
2. Create IGW
  1. Name
  2. Attach it to our VPC
3. Create Route table
  1. Name
  2. VPC ID
  3. Subnet Association : assignt the subnets
4. Add Routes
  1. Destination: 0.0.0.0/0 to IGW for public subnet
## Bastion Hosts
1. We can use a Bastion host to SSH into our private EC2 instance
2. The bastion is in the public subnet which is then connected to all other private subnets
3. Bastion Host SG must allow inbound from the internet on port 22 from restricted CIDR, for example: the public CIDR of your corporation
4. SG of EC2 instance must allow the SG of the Bastion Host, or the private IP of the Bastion Host.
## Hands – ON
1. Create EC2 instance in private Subnet
  1. Choose our own VPC
  2. Select private Subnet
  3. Create SG
    1. Name
    2. Allow SSH from custom
    3. Choose the source
    4. Descriptio: Allow SSH from the Bastion host.
# NAT Instance
1. Allow EC2 instance in private subnets to connect to internet
2. Must be launched in a public subnet
3. Must be disabled EC2 setting: Source / destination Check
4. Must have Elastic IP attached to it.
5. Route table must be configured to route traffic from private subnets to the NAT instance.
## Comments:
1. Pre – configure AMI is available
2. Not highly available / resilient setup out of the box
3. Internet traffic bandwidth depends on EC2 instance type
4. You must manage Security Groups & rules
5. You must manage SG & rules:
  1. Inboud:
    1. Allow HTTP / HTTPS traffic coming from Private Subnets
    2. Allow SSH from your home network (access is provided through IGW)
  2. Outbound:
    1. Allow HTTP / HTTPS traffic to the internet.

# NAT Gateway
1. AWS managed NAT, higher bandwidth, high availability, no administration.
2. Pay per hour for usage and bandwidth
3. NATGW is created in specific AZ, uses an Elastic IP
4. Can’t be used by EC2 instance in the same subnet ( only from other subnet)
5. Requires an IGW ( private Subnet – NAT GW – IGW )
6. 5 Gbps of bandwidth with automatic scaling up to 100 Gbps.
7. NO SG to manage / required
## NAT Gateway with High Availability
1. NAT Gateway is resilient within a single AZ.
2. Must create multiple NAT GW in multiple Azs for fault – tolerance.
3. There is no cross – AZ failover needed because if an AZ goes down it doesn’t need NAT.
## Hands – ON
1. Name
2. Public Subnet
3. Connectivity Type: public
4. Elastic IP
5. Created
6. Route Tables:
  1. Destination 0.0.0.0/0 to NAT GW

# Security Groups & NACLs
1. NACL is stateless
2. SG is stateful
3. 1 NACL per subnet.
4. You define NACL rules:
  1. Rules have a number (1 – 32766) higher precedence with a lower number
  2. First rule match will drive the decision
  3. The last rule is an asterisk (*) and denies a request in case of no rule match
  4. AWS recommends adding rules by increment of 100
5. Newly created NACL will deny everything
6. NACL are a great way of blocking a specific IP address at subnet level
## Default NACL
Accepts everything inbound / outbound with the subnets it’s associated with.
## Ephermeral Ports
1. Clients connect to a defined port, and expect a response on an ephermal port
2. Different OS use different port ranges examples:
  1. IANA & MS windows 10 – 49152 to 65535
  2. Many Linux Kernels – 32768 to 60999

# VPC Peering
1. Privately connect 2 VPCs using AWS network
2. Make them behave as if they were in the same network
3. Must not have overlapping CIDR
4. Connection is Not transitive i.e. every VPC must have vpc peering enable if they want to communicate with each other
5. We must update route tables in each VPC’s subnet to ensure EC2 instances can communicate with each other.
## Hands – ON
1. Name
2. VPC ID
3. 2nd VPC
4. Route table
  1. Public route table
    1. CIDR for 2nd VPC to peering connection
  2. Go to Demo VPC rout table
    1. CIDR for our 1st VPC to peering connection